## Slide 1: CS 211 Computer Architecture Lab (MIPS Assembly Programming) Sharad Sinha sharad@iitgoa.ac.in
  1

## Slide 2
  2
ALU- arithmetic operations
  arithmetic operations: add, sub, addi, subi and their variants
What is the difference between add and addu?
When overflow occurs in case of add and sub, the result is not stored in the destination but an exception is raised. addu does the same operations as add but ignores overflows and the result is stored in the destination.
Instruction | Syntax | Meaning
add | add $rd, $rs, $rt | $rd  $rs + $rt
subtract | sub $rd, $rs, $rt | $rd  $rs - $rt
addu unsigned | addu $rd, $rs, $rt | $rd  $rs + $rt
add immediate | addi $rt, $rs, imm | $rt  $rs + imm
add immediate unsigned | addiu $rt, $rs, imm | $rt  $rs + imm

## Slide 3
  3
ALU- logical operations
  Logical operations: AND, OR, XOR, ANDI and their variants
Instruction | Syntax | Meaning
AND | and $rd, $rs, $rt | $rd  $rs & $rt
OR | or $rd, $rs, $rt | $rd  $rs ¦ $rt
XOR | xor $rd, $rs, $rt | $rd  $rs ^ $rt
AND immediate | andi $rt, $rs, imm | $rt  $rs & imm
OR immediate | ori $rt, $rs, imm | $rt  $rs ¦ imm
XOR immediate | xori $rt, $rs, imm | $rt  $rs ^ imm

## Slide 4
  4
ALU- Shift operations
  Shift operations: srl,sll,sra and their variants
Instruction | Syntax | Meaning
Shift left logical | sll $rd, $rs, h | $rd  $rs <<h
Shift right logical | srl $rd, $rs, h | $rd  $rs >> h
Shift right arithmetic | sra $rd, $rs, h | $rd  $rs >> h
function
rd
rt
rs
opcode
Shamt (h)
The sign bit is
shifted in.
Operation | Y
3-bit shift right logical | 0 0 0 a7 a6 a5 a4 a3
3-bit shift right arithmetic | a7 a7 a7 a7 a6 a5 a4 a3
3-bit shift left logical | a4 a3 a2 a1 a0 0 0 0
Let $rs = a7a6a5a4a3a2a1a0
The shift amount, h, is 3 bits

## Slide 5
  5
Data transfer operations
  Data transfer operations: LW, SW, LB, SB
Instruction | Syntax | Meaning
Load word | lw $rt, imm($rs) | $rt  mem([$rs]+imm)
Store word | sw $rt, imm($rs) | mem([$rs] + imm) $rt
Load byte | lb $rt, imm($rs) | $rt  mem([$rs] + imm)
Store byte | sb $rt, imm($rs) | mem([$rs] + imm) $rt

## Slide 6
“la” (LOAD ADDRESS) la $s0 0x2110003d ->
Can be executed by 2 MIPS instructions:
  lui $s0,0x2110 , meaning $s0 (imm<<16):
  “load upper immediate” instruction shifts the upper two bytes of the address to left by 16 bits and loads the shifted word into destination register
  ori $s0,0x003d , meaning $s0  0x 2110 0000 OR 0000 003d:
  “OR immediate” instruction does the OR operation and loads the result into destination register
“move” is also a pseudo-instruction:
Move $t1, $t2 can be realized by add $t1, $t2, $zero
The null operation NOP or NOOP effectively does nothing, but just increments the PC by 4: can be realized by
  add $zero, $zero, $zero or
  sll $zero, $zero, $zero
  6
Pseudo instructions

## Slide 7
To multiply two integers
  Use: MULT/MULTU instruction
  Result is stored in HI and LO registers
To move the result in HI and LO registers
  Use mflo d
  Use mfhi d
  Where, d is a destination register
  7
MULT Instruction

## Slide 8
Bit wise AND
1010
1111
1010
2^32 x (2^16)
2^48
32 bits long = word
8 bit long = byte
16 bits long = half word
int A[10] A[0] A[1] A[2]
1001
0011
1001
1100
0000
1111
1100
1101

## Slide 9
High Level Programming Languages
  C, C++, Java, Python etc.
Low Level Programming Languages
  Assembly Language
Machine Level Language
  Binary representation
  FPU – Floating Point Unit